BRONZE FRETS

_____________________________________________________________________________

SINTOMS bronze frets provide a musical instrument with high quality and natural sound.

The sound of bells made of bell bronze can reach any distant place of any locality gathering people together.

SINTOMS company studied the secrets of bell bronze and developed the manufacture of frets made of that material with 2 crown types: conventional type and frill type (see the picture).

Picture. Crown types of bronze frets

Bronze frets manufactured by SINTOMS company appeared to be a real masterpiece of fretwire creation, standing out among other frets for the following advantageous characteristics:

- WEAR RESISTANCE

- PROLONGED SUSTAIN

- IMPROVED ARTICULATION

- WELL-BALANCED SOUND

- AESTHETICS

It was noted by luthiers who mounted those frets on their guitars as well as by musicians who play on musical instruments with those frets, that the price of an instrument becomes approximately 10 times higher (a significant increase) taking into account the advantages mentioned above.

Explanation of the characteristics

- WEAR RESISTANCE

Those musicians who often give concerts and practice intensive play on their musical instruments face a problem of fast deterioration (wear-out) of serial frets, mounted by a manufacturer.

Thereby musicians have to make re-fretting procedure every 3-5 years (sometimes more frequently).  A fingerboard which holds frets can bear 3-4 of such re-fretting jobs. After that fret-slots deteriorate and a fingerboard becomes inapplicable for repair.

SINTOMS frets from bell bronze are much harder and have high wear-resistance properties in comparison with serial frets of manufactures.

Bronze frets, especially frets of frill type, allow the increase of time-interval between replacements of worn-out frets in 7-10 times.

For example, Belarusian musician Vladimir Maisiuk, who plays on an acoustic guitar Taylor with strings of high tension (12-56) and with SINTOMS bronze frets, playing 3-4 hours a day within the period of 5 years already, do not see any deterioration of the frets yet.

- PROLONGED SUSTAIN

SINTOMS frets from bell bronze, especially of frill type, have an optimal combination of shape and weight which prolongs sustain of a musical instrument, provides a more clear sound throughout the full sound range of a musical instrument and facilitates the sound-producing techniques.

- IMPROVED ARTICULATION

Very often guitars with factory-mounted frets can sound well while extracting some specific sounds, but the same sounds are not heard enough when playing a melody (in mix).

SINTOMS bronze frets make a sound more articulate, clear and focused, they absorb the sound less at low and medium frequencies.

- WELL-BALANCED SOUND

Experienced musicians when playing melody on a guitar with factory frets can hear that the sound is not natural and balanced enough, sometimes the sound can even be “dim”. Experiments on replacing sensors (sound-receivers) usually change nothing in that case.

SINTOMS frets from bell bronze make the sound of a musical instrument more balanced and natural while playing a melody.

- AESTHETICS

Golden color of SINTOMS bronze frets perfectly matches with gold-plated or chrome-plated accessories of a premium-class musical instrument.

# Text boxes

Conventional Type

Frill type

(see next page)